## Slide 1: Toolbox for Engineering Design Sensitivity - TEDS
Jiannan Yang
jy419@cam.ac.uk
Dec 2020

## Slide 2
Let’s start from Digital Twins …
https://www.cdbb.cam.ac.uk/
The definitions of digital twins are not unique. Here is one description of digital twins from Centre for Digital Build Britain. No matter what is the definition, one thing we agree is that DTs provide insights so that informed decisions can be made. But how to extract most useful information from digital twins? DTs are being built across different sectors, our focus is to develop metric toolbox for digital twins to support decision making
Metric Toolbox
Decisions

## Slide 3: Toolbox for engineering design sensitivity (TEDS)
https://www.cdbb.cam.ac.uk/
TEDS
Design Sensitivity
In this presentation, I discuss in details a sensitivity toolbox (TEDS) to identify most important parameters in design

## Slide 4: Toolbox for engineering design sensitivity (TEDS)
A quick overview of the key features of TEDS
  identifies most influential random design variables
  non-intrusive toolbox because it wraps around black box digital twins and computational simulations
  provides both KPI-based and KPI-free sensitivities
Black Box Digital Twin
TEDS
Design KPI
KPI-free Sensitivity
KPI-based Sensitivity
KPI: Key performance indicator
TEDS available in both Matlab and Python

## Slide 5: Overview of the contents
Slide 6 : brief background of our current project
Slides 7 – 10 : design in the presence of uncertainties
Slides 11 – 17: some background on uncertainty and sensitivity analysis
Slides 18 – 26: mathematical details for the sensitivity toolbox
Slides 27 – 39: numerical results for an application of the toolbox
Slide 40: conclusions

## Slide 6
Some background of the project
At Cambridge, we look at design in the presence of uncertainties
https://digitwin.ac.uk/

## Slide 7
Design in the presence of uncertainties is a really broad area. Although the proposed methodology can be potentially applied to different sectors, let’s use an example to have a more concrete idea of what we are trying to do here. We have chosen offshore structure design as our examples because uncertainty considerations are important in the industrial design process of offshore structures.
Design in the presence of uncertainties

## Slide 8
Uncertain material property, probably due to manufacturing
Uncertain ocean wave heights which can be stochastic by nature, and uncertain structure/fluid interaction coefficients due to a lack of complete underlying physics
A marine riser is a conduit that extracts subsea oil to a surface platform. This example with a marine riser highlights the ubiquitous role of uncertainties for engineering design. I will use the marine riser as an example throughout the presentation (details of the dynamic model for the riser is given in the appendix )
Design in the presence of uncertainties
Uncertain force exerted by the floating platform onto the riser, depending on operation condition
Uncertain soil conditions at the sea bed

## Slide 9
Design in the presence of uncertainties
Where are the uncertainties in the whole lifecycle?

## Slide 10
Operation & Maintenance
Commissioning
Manufacturing
Design
Uncertainties
Digital Twins
Design Metrics
Design Decisions
Design in the presence of uncertainties
From the riser example, we could generalise the view a bit and look at the engineering process more abstractly. Taking account of uncertainties in the design process allows us to work towards ‘life cycle design’. Digital twins (robustly validated computational models) are increasingly used in the design. However, to make informed design decisions, the key is to provide suitable metrics of the design.

## Slide 11: Design metric - sensitivity to uncertainties
One of the most important design metric is the sensitivity to uncertainties

## Slide 12: Design metric - sensitivity to uncertainties
Black Box Digital Twin
Uncertain Input
Quantity of Interest
Sensitivities
Uncertainties
In the presence of uncertainty, the 1st step is to propagate the uncertainties through the digital twin and quantify the resulted uncertainties in the design output. This is often done using Monte Carlo methods. Once uncertainties are quantified in the design, it is desirable to conduct sensitivity analysis to understand the relative importance of the different sources of uncertainties.

## Slide 13: Uncertainty and sensitivity analysis
Black Box Digital Twin
Uncertain Input
Quantity of Interest
Inertia coefficient [Ca]
Bending stress
Riser material density [ρ]
Riser young’s modulus [E]
Uncertain Input
Drag coefficient [Cd]
Displacement
Rotation
Uncertain output
Design Sensitivities

## Slide 14: Uncertainty and sensitivity analysis
If Monte Carlo methods are used for uncertainty analysis where a large number of samples are generated , we can produce scatter plots between the uncertain inputs and outputs from the simulated samples. And this is often the most straightforward and effective way to look at sensitivities!
Black Box Digital Twin
Uncertain Input
Quantity of Interest
Uncertainties
Sensitivities

## Slide 15: Uncertainty and sensitivity analysis
There seems a strong dependency of the max stress along the riser on Ca and weak dependency on E
However, take a closer look, the range of Ca has more than doubled, while for E, there is only about 20% variable of its values. So which one is more important?
Take an example of scatter plot here for the max bending stress along the riser, against a few of the uncertain inputs.
The random bending stress is position dependent. It is of engineering interest to look at the max stress along the riser and how does it relate to the uncertain inputs.
Max stress

## Slide 16: Uncertainty and sensitivity analysis
From this example, we see that if the scatter plots are available , it is worth to have a look at it.
The scatter plots provide rich information about the relationship between inputs and outputs!
However, it can be overwhelming for large number of variables. Even for a few variables, as shown in the example here, a lot of analyses (e.g. regression analysis) are needed!

## Slide 17: Uncertainty and sensitivity analysis
In design, it would be quite useful to have metrics that provide more compact information for designers!

## Slide 18: Parametric sensitivity
Let’s take a minute and think about what is the sensitivity to the random inputs? The most natural way is to compute the derivative of y to x. However, the function of interest is often not differentiable, not to mention black box models! To overcome this issue, let's make an assumption that the input uncertain variables can be described by parametric distribution models, in other words, we can use mean and variance to describe entire distribution if the underlying distribution is assumed to be Gaussian. This is not an unreasonable assumption because most statistical methods are parametric. When you collect more information about an uncertain variable, for example by doing some experiments, it is the distribution parameters like mean and variance that will change.
Black Box Digital Twin
Uncertain Input
Quantity of Interest
Sensitivities ?
parametric distribution

## Slide 19: Parametric sensitivity
So why not look at directly at the sensitivity of the output to distribution parameters of the uncertain variables? It turns out that taking this view, there is a numerical trick called Likelihood Ratio method that will make things much easier, because the gradient information is obtained basically free (in terms of computational cost). Also, distribution functions are more likely to be differentiable.
Uncertain Input
Quantity of Interest
Black Box Digital Twin
Distribution Parameter
Sensitivities
Free of charge to get gradient! Because this term is often available analytically
represents mathematical average

## Slide 20: Parametric sensitivity
Black Box Digital Twin
Uncertain Input
Quantity of Interest
Distribution Parameter
Sensitivity to parameter b
More generally, we can look at sensitivities of any function of the random design outputs to the parameters b.
Function of the output

## Slide 21: Sensitivity in the design context
KPI-based:
Probability of failure with 80 years design life and how sensitive of it to uncertainties?
KPI-free
How is the distribution of the random bending stress affected by input uncertainties?
Concept design
Detailed design
Now that we have found the appropriate sensitivity that can be easily computed, we can implement that for design. So first we take a look at what kind of sensitivity information are needed in design? In the design context, there are two different types of scenarios where we would be interested to understand the sensitivity. For existing design or final stages of the design process, we normally have a specified design target or KPI. What we are interested is to quantify the probability that the design would fail to meet the KPI, failure probability Pf(y>y0). On the other hand, for new designs or at early design stage, a clear design target is not normally fixed. What we are interested here is the general distribution of the designed response.
and
and
KPI: Key performance indicator

## Slide 22: Mathematical framework for sensitivity
Given the response, what is the probability that the design will not satisfy the specified KP ? In other words, what is the probability of failure for the given KPI?
KPI-based sensitivity
A row vector with jth element the partial derivative with respect to parameter bj
Sensitivity is the normalised gradient vector, which is unitless so that we can compare different parameters, even their values are of many orders of magnitude different (e.g. E is in the order of 10^9, and Ca is in the order of 10^0 )
Normalize
KPI Sensitivity

## Slide 23: Mathematical framework for sensitivity
This is a random variable because y is random
Mean value is zero !
We need to take a closer look at the variance!
KPI-free sensitivity
Normalize
variance
mean
(scalar notation is used here to keep things simple)
KPI-free Sensitivity

## Slide 24: Mathematical framework for sensitivity
Fisher Information Matrix, a square matrix of dimension n, where n is the number of parameter b
KPI-free sensitivity
Let’s take a closer look at the variance term. It turns out that this is Fisher Information that is widely used in statistics
Ronald Fisher 1912.jpg
Multiple variable case

## Slide 25: Mathematical framework for sensitivity
Fisher matrix is a covariance matrix
What does this mean? It means that we try to measure the spread of the sensitivity at different realizations of our random output (note that the mean value of the sensitivity is zero)
With the covariance matrix, we can look at the principal directions for the sensitivity (the most sensitive directions), by computing the eigenvectors of the Fisher matrix (q is the eigenvector and λ is the eigenvalue). The eigenvectors (directions) with largest eigenvalues then point out the most important parameters that we should focus on to reduce uncertainties.
KPI-free sensitivity
Change to covariance notation

## Slide 26: Toolbox for engineering design sensitivity (TEDS)
In summary, we have developed a toolbox to calculate sensitivity to uncertainties in the design. It can be either KPI based or KPI free.
As to be shown in the example results, these two are correlated for the same quantity of interest. Therefore, design ‘surprises’ are minimized even KPIs only specified quite late in the design.
Black Box Digital Twin
TEDS
Design KPI
KPI-free Sensitivity
KPI-based Sensitivity
KPI: Key performance indicator

## Slide 27: Example application of TEDS
We have covered the details of what is inside the toolbox TEDS.
No more equations, let’s have a look at some example results.

## Slide 28: Example results
Design KPI:
80 years service without fatigue failure
Distribution of the max bending stress along the riser
To have a better idea of how this toolbox is applied, we analyse an example on design of a marine riser.
Black Box Digital Twin
TEDS
Design KPI
KPI-free Sensitivity
KPI-based Sensitivity

## Slide 29: Example results
Random Variable |  | Mean | Standard deviation
Morison’s equation added mass coefficient | Ca [-] | 1.5 | 0.3
Morison’s equation drag coefficient | Cd [-] | 1.1 | 0.22
Marine riser steel density | ρ [kg/m−3] | 7840 | 392
Marine riser Young’s modulus | E [GPa] | 200 | 10
Riser internal oil density | ρo [kg/m−3] | 920 | 92
Marine riser top tension | T0 [kN] | 4905 | 490.5
Material S-N curve coefficients | α [GPa] | 199 | 19.9
 | δ [-] | 3 | 0.3
Mean and standard deviation values for the random input variables (Gaussian)
S-N law

## Slide 30: Example results
What is the sensitivity of design KPI: 80 years service without fatigue failure
The sensitivity results tells us which parameter is important for the specified KPI: bigger value of r means the fatigue failure is more sensitive to it.
The results shown here do make sense because for example:
δ is quite important because number of cycles to fatigue failure depends on stress to the power of δ
E is important because bending stress is proportional to it
KPI-based sensitivity

## Slide 31: Example results
What is the sensitivity of the general distribution of the max bending stress? Fisher Eigenvectors
First, only one dominant eigenvector in this case (see magnitude of eigenvalues below)  this is the most sensitive direction
Second, as compared to the scatter plot at the beginning of the presentation, we have Ca and E as important ones, but E of similar importance as Ca, unlike the scatter plot where it seemed that Ca is dominant
KPI-free sensitivity

## Slide 32: Example results
TEDS
Design KPI
KPI-free Sensitivity
KPI-based Sensitivity
How are these two types of sensitivity related in this case?
Take dot product between the failure sensitivity vector and different eigenvectors to compute the projection
In this case, the similarity (shape) between 1st eigenvector of KPIs free sensitivity and KPI-based sensitivity is the highest

## Slide 33: Example results
TEDS
KPI-free Sensitivity
KPI-based Sensitivity
Clearly quite similar in this case! This is expected because both sensitivities are related to high stress levels. However, the level of similarity is case dependent.

## Slide 34: More Example Results – Displacement Response
Design KPI:
90% of all simulated displacement response is below a given threshold
Distribution of max displacement along the riser
Black Box Digital Twin
TEDS
Design KPI
KPI-free Sensitivity
KPI-based Sensitivity

## Slide 35: More Example Results – Displacement Response
TEDS
KPI-free Sensitivity
KPI-based Sensitivity
Another ‘good’ example that projection is dominated by 1st eigenvector

## Slide 36: More Results – General Case
Three Design KPI:
Fatigue failure
Excessive displacement
Excessive rotation
Joint distribution of max stress, displacement and rotation along the riser
Black Box Digital Twin
TEDS
Design KPI
KPI-free Sensitivity
KPI-based Sensitivity

## Slide 37: More Results – General Case
TEDS
KPI-based Sensitivity
Three Design KPI:
Fatigue failure
Excessive displacement
Excessive rotation
Different important parameters for the three failure modes

## Slide 38: More Results – General Case
TEDS
KPI-free Sensitivity
Joint distribution of max stress, displacement and rotation along the riser

## Slide 39: More Results – General Case
KPI-free Sensitivity
KPI-based Sensitivity
This is a counter example that the two sensitivities are not always pointing exactly to the same direction !
However, it can be seen that the projections of the KPI-based sensitivities are still dominated by the eigenvectors of Fisher matrix, with large eigenvalues !
These large ones give you good directions for design at early stages where KPIs are not fixed!

## Slide 40: Conclusions
TEDS – a toolbox for engineering design sensitivities
  a probabilistic model that quantifies sensitivity to design uncertainties
  can be wrapped around black box digital twins and computational simulations
  provides both KPI-based and KPI-free sensitivities
Yet applied on real industrial cases, a few limitations expected:
  Only parametric distribution for design input, where a variety of uncertainty types are needed for industrial applications
  Still a gap to design decisions: is it worth investment to reduce uncertainties?
Black Box Digital Twin
TEDS
Design KPI
KPI-free Sensitivity
KPI-based Sensitivity
KPI: Key performance indicator
TEDS available in both Matlab and Python

## Slide 41
Jiannan Yang
jy419@cam.ac.uk
Dec 2020
Any questions/comments:
jy419@cam.ac.uk